## Slide 1: Graph Neural Network and Reinforcement Learning in EDA and beyond
Callie Hao
Assistant Professor
ECE, Georgia Institute of Technology
  Sharc-lab @ Georgia Tech https://sharclab.ece.gatech.edu/

## Slide 2: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 3: Acknowledgement
Nan Wu
University of California, Santa Barbara
Yuan Xie
University of California, Santa Barbara
Pan Li
Purdue University
… and myself
(Just to fill up the space)

## Slide 4: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 5: What is Graph Neural Network (GNN)
Traditional neural networks are designed for simple sequences & grids
[Slide credit: http://web.stanford.edu/class/cs224w]
Speech/Text

## Slide 6: What is Graph Neural Network (GNN)
Reality: A lot of real-world data does not “live” on grids
  Arbitrary size and complex topological structure
  No fixed node ordering or reference point
  Often dynamic and have multimodal features
Image credit: Madhavicmu / Wikimedia Commons/CC-BY-SA-4.0
Social Networks
Economic Networks
Protein Interaction Networks

## Slide 7: What is Graph Neural Network (GNN)
[Slide credit: Structured deep models: Deep learning on graphs and beyond]
Main Idea: Pass massages between pairs of nodes and agglomerate

## Slide 8: How is GNN Computed (e.g., GCN)
Key idea: Generate node embeddings based on local network neighborhoods
  Node embedding: a vector to represent the node features
[Slide credit: http://web.stanford.edu/class/cs224w]
MLP
MLP
MLP
MLP

## Slide 9: Inductive Capability of GNNs
Model parameters are shared for all nodes
Model can generalize to unseen nodes and entirely unseen graphs
[Slide credit: http://web.stanford.edu/class/cs224w]

## Slide 10: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 11: What is Reinforcement Learning (RL)
An agent learns in an interactive environment by trial and error using feedback from its own actions and experiences
  Suitable to handle control problems or sequential decision-making processes
  Can explore design space proactively and intelligently
  Agent behaviors are optimized by embedding optimization goals into reward functions
[Slide credit: https://arxiv.org/pdf/2102.07952.pdf]

## Slide 12: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 13: What is High Level Synthesis (HLS)
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
HLS Tools
REG
in
+
*
REG
in
+
*
out
REG
in
+
*
  C / C++, Chisel, …
  Verilog, VHDL, …
  Software Specification and Program
  Circuit (ASIC, FPGA) Design
High-Level Synthesis
Logic Synthesis
Physical Synthesis

## Slide 14: What is High Level Synthesis (HLS)
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
for (i=1; i<=c;)
a = a++;
b = x*2-a;
a = y+b/3;
HLS Tools
REG
in
+
*
REG
in
+
*
out
REG
in
+
*
  C / C++, Chisel, …
  Verilog, VHDL, …
  Software Specification and Program
  Circuit (ASIC, FPGA) Design
High-Level Synthesis
Logic Synthesis
Physical Synthesis
Why HLS?
  Easy programming: C/C++/Python v.s. Verilog
  Fast → productivity
  Promote device usage
  More optimization opportunities at higher level

## Slide 15: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 16: HLS: Program-to-Circuit
Programs are translated to Data Flow Graphs (DFGs) as the Intermediate Representation (IR)
Techniques applied to DFGs: operation scheduling, resource allocation, resource binding, etc.
Finally translated to register-transfer level (RTL) Circuit
+
+
*
*
*
+
*
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Data Flow Graph (DFG)
Program
ADD
MUL
REG
REG
REG
REG
RTL (Circuit)

## Slide 17: HLS: Program-to-Circuit Challenges
+
+
*
*
*
+
*
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Data Flow Graph (DFG)
Program
RTL (Circuit)
Program-to-Circuit
  Hard-to-predict RTL circuit quality
  Multi-objective trade-offs
  Manual code transformation
1
2
3
ADD
MUL
REG
REG
REG
REG

## Slide 18: Challenge 1: Hard-to-predict RTL Quality
Getting actual circuit quality after implementation is very time-consuming
  E.g,. resource usage, critical path timing
  How about quality prediction?
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Program
RTL (Circuit)
ADD
MUL
REG
REG
REG
REG
Actual Implementation
Hours to days…
A few Seconds
+
+
*
*
*
+
*
Data Flow Graph (DFG)
Minutes to hours

## Slide 19: Challenge 1: Hard-to-predict RTL Quality
Getting actual circuit quality after implementation is very time-consuming
  E.g,. resource usage, critical path timing
  How about quality prediction?
RTL design quality is hard to predict, especially for irregular data paths
  Existing HLS tools’ estimation sometimes can be far from accurate
  Analytical-model-based predictors only work for well-structured data flows
  ML-based predictors requires abundant features after design synthesis and/or implementation
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Program
RTL (Circuit)
ADD
MUL
REG
REG
REG
REG
Actual Implementation
Hours to days…
A few Seconds
+
+
*
*
*
+
*
Data Flow Graph (DFG)
Minutes to hours

## Slide 20: Motivation 1: Predict Impl. Quality Accurately
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Program
RTL (Circuit)
ADD
MUL
REG
REG
REG
REG
Actual Implementation
Hours to days…
A few Seconds
+
+
*
*
*
+
*
Data Flow Graph (DFG)
Minutes to hours
Extract the DFG…
… and predict the implementation quality accurately

## Slide 21: Solution 1: Use Graph Neural Network (GNN)
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Program
RTL (Circuit)
ADD
MUL
REG
REG
REG
REG
Actual Implementation
Hours to days…
A few Seconds
+
+
*
*
*
+
*
Data Flow Graph (DFG)
Minutes to hours
Extract the DFG…
… and predict the implementation quality accurately
Use Graph Neural Networks!
…and they can generalize to unseen programs!

## Slide 22: HLS: Program-to-Circuit Challenges
+
+
*
*
*
+
*
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Data Flow Graph (DFG)
Program
RTL (Circuit)
Program-to-Circuit
  Hard-to-predict RTL circuit quality
  Multi-objective trade-offs
  Manual code transformation
1
2
3
ADD
MUL
REG
REG
REG
REG

## Slide 23: Challenge 2: Multi-objective Trade-offs
(Example) Constraints
  Number of DSPs on FPGA
(Example) Design Choices
  Each multiplication: use DSP or LUTs?
Objectives
  Meeting user-specified constraint
  Minimize other resources (area)
  Optimizing critical path timing (clock frequency)
DSP=2

## Slide 24: Challenge 2: Multi-objective Trade-offs
(Example) Constraints
  Number of DSPs on FPGA
(Example) Design Choices
  Each multiplication: use DSP or LUTs?
Operations using DSPs
Operations using LUTs
DSP: 4
Latency: 3
(a) HLS default solution
DSP=2
Objectives
  Meeting user-specified constraint
  Minimize other resources (area)
  Optimizing critical path timing (clock frequency)

## Slide 25: Challenge 2: Multi-objective Trade-offs
(Example) Constraints
  Number of DSPs on FPGA
(Example) Design Choices
  Each multiplication: use DSP or LUTs?
Operations using DSPs
Operations using LUTs
DSP: 4
Latency: 3
(a) HLS default solution
DSP: 2
Latency: 4
(b) HLS solution with naïve constraints
DSP=2
Objectives
  Meeting user-specified constraint
  Minimize other resources (area)
  Optimizing critical path timing (clock frequency)

## Slide 26: Challenge 2: Multi-objective Trade-offs
(Example) Constraints
  Number of DSPs on FPGA
(Example) Design Choices
  Each multiplication: use DSP or LUTs?
Operations using DSPs
Operations using LUTs
DSP: 4
Latency: 3
(a) HLS default solution
DSP: 2
Latency: 4
(b) HLS solution with naïve constraints
DSP=2
Objectives
  Meeting user-specified constraint
  Minimize other resources (area)
  Optimizing critical path timing (clock frequency)
  Sacrificing latency (# of clock cycles)?

## Slide 27: Challenge 2: Multi-objective Trade-offs
(Example) Constraints
  Number of DSPs on FPGA
(Example) Design Choices
  Each multiplication: use DSP or LUTs?
Operations using DSPs
Operations using LUTs
DSP: 4
Latency: 3
(a) HLS default solution
DSP: 2
Latency: 4
(b) HLS solution with naïve constraints
(c) A better solution
DSP: 2
Latency: 3
DSP=2
Objectives
  Meeting user-specified constraint
  Minimize other resources (area)
  Optimizing critical path timing (clock frequency)
  Sacrificing latency (# of clock cycles)?

## Slide 28: Motivation 2: Automated DSE
(c) A better solution
Initial DFG
Automatically find a best resource allocation that:
  Learns to assign resources
  Meet user-specified constraints
  Trade-off between resource and critical path timing
  Do not sacrifice latency

## Slide 29: Solution 2: Reinforcement Learning (RL)
(c) A better solution
Initial DFG
Use Reinforcement Learning (RL)!
Use Reinforcement Learning (RL)!

## Slide 30: HLS: Program-to-Circuit Challenges
+
+
*
*
*
+
*
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Data Flow Graph (DFG)
Program
RTL (Circuit)
Program-to-Circuit
  Hard-to-predict RTL circuit quality
  Multi-objective trade-offs
  Manual code transformation
1
2
3
ADD
MUL
REG
REG
REG
REG

## Slide 31: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations

## Slide 32: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
for (int i = 0; i < 8; i++)
{
sum += a[i] * b[i];
}
If DSP constraint is 3?
HLS Method | Cycles | DSP | LUTs | CP (ns)
Original | 17 | 1 | 75 | 4.07
Unroll (factor=8, complete) | 2 | 8 | 100 | 5.04
Unroll (factor=4) | 4 | 4 | 87 | 4.83
Unroll (factor=3) | 8 | 3 | 109 | 7.44
Unroll + allocation (limit=3) | 4 | 6 | 168 | 8.76
The best we can get: DSP = 3, Cycles = 8

## Slide 33: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
for (int i = 0; i < 8; i++)
{
sum += a[i] * b[i];
}
If DSP constraint is 3?
HLS Method | Cycles | DSP | LUTs | CP (ns)
Original | 17 | 1 | 75 | 4.07
Unroll (factor=8, complete) | 2 | 8 | 100 | 5.04
Unroll (factor=4) | 4 | 4 | 87 | 4.83
Unroll (factor=3) | 8 | 3 | 109 | 7.44
Unroll + allocation (limit=3) | 4 | 6 | 168 | 8.76
Code Transformation (CT) | 2 | 8 | 100 | 5.03
int m1 = a[0] * b[0];
int m2 = a[1] * b[1];
…
int m8 = a[7] * b[7];
int m9 = m1 + m2;
…
Transformed Code

## Slide 34: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
for (int i = 0; i < 8; i++)
{
sum += a[i] * b[i];
}
If DSP constraint is 3?
HLS Method | Cycles | DSP | LUTs | CP (ns)
Original | 17 | 1 | 75 | 4.07
Unroll (factor=8, complete) | 2 | 8 | 100 | 5.04
Unroll (factor=4) | 4 | 4 | 87 | 4.83
Unroll (factor=3) | 8 | 3 | 109 | 7.44
Unroll + allocation (limit=3) | 4 | 6 | 168 | 8.76
Code Transformation (CT) | 2 | 8 | 100 | 5.03
CT + resource (5 Mul_LUT) | 2 | 2 | 1742 | 4.24
CT + resource (4 Mul_LUT) | 2 | 2 | 1741 | 4.01
CT + resource (3 Mul_LUT) | 2 | 3 | 1461 | 3.98
int m1 = a[0] * b[0];
int m2 = a[1] * b[1];
…
int m8 = a[7] * b[7];
int m9 = m1 + m2;
…
The best we can get: DSP = 3, Cycles = 2

## Slide 35: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
for (int i = 0; i < 8; i++)
{
sum += a[i] * b[i];
}
If DSP constraint is 3?
HLS Method | Cycles | DSP | LUTs | CP (ns)
Original | 17 | 1 | 75 | 4.07
Unroll (factor=8, complete) | 2 | 8 | 100 | 5.04
Unroll (factor=4) | 4 | 4 | 87 | 4.83
Unroll (factor=3) | 8 | 3 | 109 | 7.44
Unroll + allocation (limit=3) | 4 | 6 | 168 | 8.76
Code Transformation (CT) | 2 | 8 | 100 | 5.03
CT + resource (5 Mul_LUT) | 2 | 2 | 1742 | 4.24
CT + resource (4 Mul_LUT) | 2 | 2 | 1741 | 4.01
CT + resource (3 Mul_LUT) | 2 | 3 | 1461 | 3.98
int m1 = a[0] * b[0];
int m2 = a[1] * b[1];
…
int m8 = a[7] * b[7];
int m9 = m1 + m2;
…
The best we can get: DSP = 3, Cycles = 2
DSP = 3, Cycles = 8
v.s.

## Slide 36: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
for (int i = 0; i < 8; i++)
{
sum += a[i] * b[i];
}
If DSP constraint is 3?
for (int i = 0; i < 17; i++) {
for (int j = i; j < 23; j+=2) {
sum += a[i] * b[j];
}
}
If DSP constraint is 13?

## Slide 37: Challenge 3: Manual Code Transformation
High level abstraction in HLS can conceal optimization opportunities
  Structured HLS coding style hinders fine-grained optimization
    Loops, function calls, etc.
  Irregular logic requires manual or complicated code transformations
Motivation: Need better performance and more flexible optimization choices
Solution: Code transformation

## Slide 38: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 39: IronMan: GNN + RL for HLS Predict & DSE
IronMan： An end-to-end framework integrating CT, GPP, and RLMD targeting HLS (Program-to-Circuit)
Wu, Nan, Yuan Xie, and Cong Hao. GLSVLSI, 2021

## Slide 40: IronMan: GNN + RL for HLS Predict & DSE
Code Transformer (CT) → Challenge 3
Manual CT
Expose more optimization opportunities

## Slide 41: IronMan: GNN + RL for HLS Predict & DSE
GPP→Challenge 1
Hard-to-predict RTL Quality
Impl. quality prediction
Code Transformer (CT) → Challenge 3
Manual CT
Expose more optimization opportunities

## Slide 42: IronMan: GNN + RL for HLS Predict & DSE
GPP→Challenge 1
Hard-to-predict RTL Quality
Impl. quality prediction
RLMD → Challenge 2
Multi-objective Trade-offs
Automated DSE
Code Transformer (CT) → Challenge 3
Manual CT
Expose more optimization opportunities

## Slide 43: IronMan: GNN + RL for HLS Predict & DSE
IRONMAN Goal (a case study):
Find a solution that strictly meets DSP constraints
Find Pareto solutions between DSP and LUT resources on FPGAs, without sacrificing latency

## Slide 44: GPP: GNN-based Performance Predictor

## Slide 45: GPP: GNN-based Performance Predictor
Generating graph representations

## Slide 46: GPP: GNN-based Performance Predictor
3 models of the same structure to separately predict LUT/DSP and CP timing
Feed-forward NN
Generating graph representations

## Slide 47: GPP: GNN-based Performance Predictor
3 models of the same structure to separately predict LUT/DSP and CP timing
Feed-forward NN
Generating graph representations
Node feature vector:
1st ~ 4th: Input / node type (, ) / output
5th ~9th: Bit-width (2~32)
10th: w/wo pragma

## Slide 48: GPP: GNN-based Performance Predictor
3 models of the same structure to separately predict LUT/DSP and CP timing
Feed-forward NN
Generating graph representations
Goal of GPP:
Provide graph embeddings of DFGs → generalize across different graphs
Provide high-accuracy performance predictions → quick evaluation of generated solutions and accelerate RL training
Node feature vector:
1st ~ 4th: Input / node type (, ) / output
5th ~9th: Bit-width (2~32)
10th: w/wo pragma

## Slide 49: RLMD: RL-based Multi-objective DSE
State: every possible partially assigned DFGs
Action: whether to assign a certain directive to the current node
Reward: a negative weighted sum of predicted resource utilization

## Slide 50: Putting GPP and RLMD Together

## Slide 51: Putting GPP and RLMD Together
Two policy optimization methods:
  Actor-critic
  Policy-gradient

## Slide 52: Putting GPP and RLMD Together
Actor: Probability distribution on actions
Critic: State-value function
Two policy optimization methods:
  Actor-critic
  Policy-gradient
Reward

## Slide 53: Experiment Setup
Dataset
  Synthetic: 47 different topologies x 100 sets of directives per topology → 4,700 graphs
  Real-world: 8 real-case benchmarks x 100 sets of directives per benchmark → 800 graphs
    Real applications come from MachSuite, CHStoneand PolyBench/C: gemm, kernel_2mm, kernel_durbin(small,large), spmv, stencil3d(small, large), and kernel_adi
Baselines
  Simulated annealing (SA), Genetic algorithm (GA), particle swarm optimization (PSO), Vivado HLS
Training
  Trained on 41 different synthetic topologies and 4 real-case benchmarks → 4,500 graphs
  Evaluated on the rest of graphs → 1,000 graphs
Evaluation
  Ground-truth and solutions are synthesized by Vivado HLS and implemented by Vivado
  Actual resource utilization (LUT/DSP) and critical path (CP) timing

## Slide 54: GPP Evaluation: Implementation Prediction
GPP predictions on resource utilization (LUT, DSP), and critical path timing (CP)

## Slide 55: GPP Evaluation: Implementation Prediction
GPP
GPP
GPP
HLS
HLS
HLS
GPP predictions on resource utilization (LUT, DSP), and critical path timing (CP)

## Slide 56: GPP Evaluation: Implementation Prediction
GPP predictions on resource utilization (LUT, DSP), and critical path timing (CP)
Reduce prediction error of Vivado HLS by 10.9x in resource and 5.7x in timing
GPP
GPP
GPP
HLS
HLS
HLS

## Slide 57: GPP Design Choices

## Slide 58: IronMan Evaluation: Pareto Solutions
GEMM
Kernel_2mm
Discussions
IronMan outperforms SA/GA/PSO by a large margin (>12.0%)
Fine-tune helps (11.6% additional reduction)
In general policy-gradient outperforms actor-critic
PG with fine-tune
AC with fine-tune
PG
AC
SA/GA/PSO
SA/GA
/PSO
SA/GA
/PSO
IronMan
IronMan

## Slide 59: IronMan Evaluation: Multi-objective Opt.
GEMM
Kernel_2mm
GEMM
Kernel_2mm
LUT : CP = 1:9 → Better Timing
LUT : CP = 9:1 → Less LUTs

## Slide 60: IronMan Evaluation: Meeting Constraints
RLMD meets user-specified constraints (# of DSPs) almost perfectly!

## Slide 61: Summary of IronMan
Independently:
  GPP achieves high prediction accuracy
  RLMD obtains Pareto solutions surpassing GA/SA/PSO
Integrated, IronMan is can:
  Help HLS tools generate higher quality solutions under user-specified constraints
  Perform flexible DSEs to provide Pareto solutions that are not currently supported by HLS tools
  Find solutions perfectly matching various DSP constraints
  Execute up to 400X faster than the heuristic algorithms and HLS tools

## Slide 62: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 63: Diving Deeper: Program-to-Circuit
x1 = a + b;
x2 = b + c;
x3 = d * e;
y1 = x1 * x2;
y2 = x2 * x3;
o1 = y1 + 5;
o2 = y1 * y2;
Program
RTL (Circuit)
ADD
MUL
REG
REG
REG
REG
Actual Implementation
Hours to days…
A few Seconds
+
+
*
*
*
+
*
Data Flow Graph (DFG)
Minutes to hours
Extract the DFG…
… and predict the implementation quality accurately
How powerful are GNNs to represent programs and to solve Program-to-Circuit problem?

## Slide 64: From IronMan to Program-to-Circuit
IronMan | Program-to-Circuit
Only MUL and ADD operations | All types of operations: arithmetic computation, memory (load/store), control (loop, branch), etc.
Data Flow Graph (DFG) | Control Data Flow Graph (CDFG)
10 node features (one-hot embedding) | More complex learnable node embeddings
2-layer GCN | 14 types of GNNs
  Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, “Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation”, arXiv, 2021

## Slide 65: Prediction Performance on DFG and CDFG

## Slide 66: Prediction Performance on DFG and CDFG
DFG v.s. CDFG

## Slide 67: Prediction Performance on DFG and CDFG

## Slide 68: Discussions (1): DFG v.s. CDFG
DFG v.s. CDFG
  CDFG size is approximately twice as large as DFG
    More difficult for graph-level regression
  CDFGs has a considerable number of loops
    Challenge the representation power of GNNs
  Control nodes/edges introduce additional complexity
Example DFG
Example CDFG
loop

## Slide 69: Discussions (2): GNN Model Choices
GNN Model Choices
  PNA and RGCN generally show superior performance
    PNA with multiple aggregators is more powerful to characterize different neighborhood information
    Relational information is important in IR graphs, representing data/control dependency
Principle Neighborhood Aggregation (PNA)
Corso, G., Cavalleri, L., Beaini, D., Liò, P. and Veličković, P., Principal Neighborhood Aggregation for Graph Nets. NeurIPS, 2020
Schlichtkrull, Michael, et al. "Modeling relational data with graph convolutional networks." European semantic web conference, 2018.
Relational Graph Convolutional Network (RGCN)

## Slide 70: Discussions (3): Global v.s. Local Information
CP Timing: shows lower error rates and better consistency between DFGs and CDFGs
  (Possibly) CP timing is insensitive to graph sizes since it captures local information between FFs
D
Q
D
Q
Combinational Logic
in
out
clk
FF1
FF2
Critical Path (CP): local information
void top_dfg(int* a, int* b, int* c)
{
*a = (*b) + 2;
int t1 = (*a) * (*b) + 4;
int t2 = t1 + (*c);
int t3 = (*b) * (t2);
*c = t1 + t2 + t3;
}
(a) Program
(c) Circuit
DSPs
n11_read
n1_port
n2_port
n13_write
n12_add
n14_mul
n15_add
n3_port
n21_write
n16_read
n17_add
n20_add
n19_add
n18_mul
(b) IR graph
SLICE
Resource: global information

## Slide 71: GNNs v.s. HLS
HLS Prediction
PNA Prediction

## Slide 72: GNNs v.s. HLS
HLS Prediction
PNA Prediction
GNNs are slightly better in resource but obviously better in CP timing, which is hard-to-predict

## Slide 73: Observed Challenges (so far…)
Generalization across graph sizes, node degrees, and out-of-distribution cases
Structural and algorithmic innovations to process heavy-loop graph topologies
  GNNs are in general fragile in loops (1-WL test)
  Small loops usually relate to memory operations and are confusing for resource estimation
Gap from classification to regression
  Most existing GNNs are for classification (node, link, graph)
  The resource/timing prediction is regression → a harder problem!

## Slide 74: Outline
Background
  Graph Neural Network (GNN)
  Reinforcement Learning (RL)
  High Level Synthesis (HLS)
HLS: Program-to-Circuit
  IRONMAN: GNN-assisted design space exploration in high-level synthesis via reinforcement learning
    Nan Wu, Yuan Xie, and Cong Hao, GLSVLSI, 2021
  Program-to-Circuit: Exploiting GNNs for Program Representation and Circuit Translation
    Nan Wu, Huake He, Yuan Xie, Pan Li, Cong Hao, arXiv, 2021
And beyond: Program-to-X
  Call for future research interests 

## Slide 75: From Program-to-Circuit to Program-to-X
Program
To
Circuit
Program
To
X

## Slide 76: From Program-to-Circuit to Program-to-X
GNN representation power for programs
  Handling loops (very typical in programs)
  Largely varied size
  …
Specific GNN design for different down-stream tasks
  Program analysis on vulnerability
  Behavior prediction
  Throughput estimation
  …
Benchmark development

## Slide 77: Summary & Thanks!
Discussed the power of GNN and RL in solving EDA problems, e.g., HLS
  IronMan!
Discussed a more general problem, Program-to-Circuit
  Hoping for more datasets, better GNNs, more domain-specific insights, etc.
The potential from Program-to-Circuit to Program-to-X
  Looking forward to seeing more works!
Contact:
  callie.hao@ece.gatech.edu
  Sharc-lab @ Georgia Tech (https://sharclab.ece.gatech.edu/)